## Slide 1
Habitat hydraulic modelling for environmental flow restoration in upland streams in Greece
European Regional Development Fund
July 2014
Habitat hydraulic modelling for environmental flow restoration in upland streams in Greece
Ch. Papadaki1, L. Ntoanidis2, S. Zogaris1, F. Martinez-Capel3, R. Muñoz-Mas3, N. Evelpidou4 and E. Dimitriou1
1,Hellenic Centre for Marine Research, Institute of Marine Biological Resources and Inland Waters, 46.7 km, Athens - Sounio Ave., 19013, Anavissos, Greece,
2D. Argyropoulos & associates, Tinou 2, 15562 Cholargos, Greece,
3, Research Institute for Integrated Management of Coastal Areas, Universitat Politècnica de València. C/ Paranimf 1, 46730 Grau de Gandia. Valencia. España,
4Faculty of Geology and Geoenvironment, National and Kapodistrian University of Athens, Panepistimiopolis, 15784 Athens, Greece

## Slide 2
Aquatic species react to changes in the hydraulic environment
Jowett 1992,
Jager et al. 1993,
Nehring and Anderson 1993,
Railsback et al. 1993,
Bovee et al. 1994,
Stalnaker et al. 1995,
Studley et al. 1995
Apply a state-of-the-art methodology for the estimation of environmental flows by predicting how different in-stream flows affect fish microhabitats
Why fish?
The aim of this study
EU Water Framework Directive (WFD)

## Slide 3
was used to determine characteristics of the stream,
in terms of depth and velocity, as a function of discharge
integrated with the hydraulic model to produce a measurement for available habitat
as a function of discharge
Basic elements of the study
originally integrated in the
Instream Flow Incremental methodology (IFIM)
Hydraulic model
Habitat Suitability Criteria Curves
One-dimensional -HEC RAS

## Slide 4
Habitat mapping for the selection of the representative study reaches in a segment of 1.5 km length
A mesoscale approach for the selection of the study reaches
Identification of several types of hydromorphological units, (i.e. pools, runs, riffles, glides, rapids) noting their location and extent, and measuring their physical attributes (width, mean depth)

## Slide 5
Athens
Study sites

## Slide 6
Location:
Mountainous part of the upper Acheloos River Basin
Why these two sites?
relatively undisturbed conditions
intense debate about the construction of small hydroelectric plants in montane rivers
Main characteristics:
Summer flows are ranging from 2 to 5 m3/sec based on past measurements of Public Power Corporation of Greece.
mean elevation: 1100 m a.s.l.
average slope: 2.5 %
Study sites

## Slide 7
Tripotamo
Mesochora upstream

## Slide 8
A detailed topographic survey was made to create a digital elevation model (DEM)
 | Substrate type | Size (mm)
1 | Vegetation | -
2 | Silt (Mud) | <0.06
3 | Sand | 0.06-2
4 | Gravel | 8 - 64
5 | Cobble | 64-264
6 | Boulder | >264

## Slide 9
Cross
sections
Bed
roughness
Manning’s N
Suitability Maps
Weighted Usable Area
(WUA)
Suitability
curves
Hydraulic Model
HEC RAS
River flows
Depth
GIS layer
Velocity
GIS layer
A short description of the method

## Slide 10
Mesochora Upstream
31 transects within a 348 m reach
(covering the channel and floodplain)
Tripotamo
27 transects within a 246 m reach
Cross sections

## Slide 11
Every cross-section was divided in sub-sections (cells) in the HEC-RAS,
then the model calculates the mean velocity at each cell
(at a given river flow and WSE)

## Slide 12
(A) Simulated Depth results (m) Mesochora Upstream |  |  | 
Q | 1 (m3/sec) | 8 (m3/sec) | 30 (m3/sec)
HEC - RAS |  |  | 
(B) Simulated Velocity results (m/sec) Mesochora Upstream |  |  | 
Q | 1 (m3/sec) | 8 (m3/sec) | 30 (m3/sec)
HEC - RAS |  |  | 
Mesochora Upstream

## Slide 13
(B) Simulated Velocity results (m/sec) Tripotamo |  |  | 
Q | 1 (m3/sec) | 10 (m3/sec) | 15 (m3/sec)
HEC - RAS |  |  | 
(A) Simulated Depth results (m) Tripotamo |  |  | 
Q | 1 (m3/sec) | 10 (m3/sec) | 15 (m3/sec)
HEC - RAS |  |  | 
Tripotamo

## Slide 14
Depth and mean velocity were converted into their corresponding values of habitat suitability index using habitat suitability curves extracted from former studies of trout habitat (Boove 1978)
Chart: Brown Trout Adult
| 0 | 0.1 | 0.2 | 0.25 | 0.29000000000000004 | 0.30000000000000004 | 0.35000000000000003 | 0.4 | 0.5 | 0.60000000000000009 | 0.66000000000000014 | 0.70000000000000007 | 0.75000000000000011 | 0.8 | 0.85000000000000009 | 0.9 | 0.95000000000000007 | 1 | 1.05 | 1.1000000000000001 | 1.1700000000000002 | 1.2 | 1.25 | 1.3 | 1.35 | 1.4 | 1.5 | 1.6 | 1.7000000000000002 | 1.7500000000000002 | 1.8 | 1.9 | 2 | 2.0499999999999998 | 2.1 | 2.15 | 2.2000000000000002 | 2.25 | 2.2999999999999998 | 2.3499999999999996 | 2.4 | 2.4499999999999997 | 2.5 | 2.6 | 2.68 | 2.7 | 2.8 | 2.9 | 2.9699999999999998 | 3 | 3.1 | 3.2 | 3.25 | 3.3 | 3.4 | 3.5 | 3.6 | 3.7 | 3.77 | 3.8 | 3.9 | 4 | 4.0999999999999996 | 4.2 | 4.3 | 4.4000000000000004 | 4.5 | 4.5999999999999996 | 4.63 | 4.7 | 4.8 | 4.9000000000000004 | 5 | 5.0999999999999996 | 5.2 | 5.21 | 5.3 | 5.4 | 5.5 | 5.57 | 5.6 | 5.7 | 5.8 | 5.9 | 6 | 6.1 | 6.2 | 6.3 | 6.4 | 6.5 | 6.7 | 6.8 | 6.9 | 7 | 9.9999999999999911
Bovee | 0 | 0.06 | 0.15 | 0.27 | 0.51 | 0.58 | 0.6 | 0.61 | 0.63 | 0.65 | 0.67 | 0.68 | 0.7 | 0.72 | 0.74 | 0.78 | 0.81 | 0.86 | 0.94 | 0.97 | 0.99 | 1 | 1 | 1
Chart: Brown Trout Adult
| 0 | 0.05 | 0.1 | 0.15000000000000002 | 0.2 | 0.25 | 0.30000000000000004 | 0.35000000000000003 | 0.4 | 0.45 | 0.5 | 0.55000000000000004 | 0.60000000000000009 | 0.65000000000000013 | 0.70000000000000007 | 0.75000000000000011 | 0.8 | 0.82000000000000006 | 0.85000000000000009 | 0.9 | 0.95000000000000007 | 1 | 1.05 | 1.07 | 1.1000000000000001 | 1.1499999999999997 | 1.2 | 1.25 | 1.3 | 1.32 | 1.35 | 1.4 | 1.45 | 1.5 | 1.55 | 1.6 | 1.6300000000000001 | 1.6500000000000001 | 1.7 | 1.75 | 1.8 | 1.85 | 1.9000000000000001 | 1.9400000000000002 | 1.9500000000000002 | 2 | 2.0499999999999998 | 2.1 | 2.15 | 2.2000000000000002 | 2.25 | 2.2999999999999998 | 2.3499999999999996 | 2.4 | 2.4499999999999997 | 2.5 | 2.6 | 2.65 | 2.7 | 2.75 | 2.8 | 2.9 | 3 | 3.1 | 3.15 | 3.2 | 3.25 | 3.3 | 3.4 | 3.4899999999999998 | 3.5 | 3.55 | 3.6 | 3.7 | 3.74 | 3.75 | 3.8 | 3.9 | 4 | 4.18 | 4.2 | 4.5999999999999996 | 5 | 5.4 | 5.55 | 5.8 | 6 | 6.2
Bovee | 1 | 1 | 0.98 | 0.95 | 0.91 | 0.81 | 0.74 | 0.68 | 0.65 | 0.62 | 0.59 | 0.57 | 0.55 | 0.5 | 0.47 | 0.44 | 0.38 | 0.33 | 0.28 | 0.23 | 0.19 | 0.15 | 0.14 | 0.11 | 0.09 | 0.07 | 0.06 | 0.05 | 0.03 | 0

## Slide 15
(C) Habitat Suitability Index |  |  | 
Q | 1 (m3/sec) | 10 (m3/sec) | 15 (m3/sec)
TRIPOTAMO |  |  | 
 | 1 (m3/sec) | 8 (m3/sec) | 30 (m3/sec)
MESOCHORA UPSTREAM |  |  | 
Maps of habitat suitability (HSI) with 4 suitability classes:
the aggregated Habitat Suitability Index (HSI) was calculated for each cell

## Slide 16
Chart: Tripotamo
| 0.4 | 0.70000000000000007 | 1 | 2.5 | 4 | 5 | 7 | 10 | 15
WUA-Adult | 646.4651 | 699.9362 | 746.5847 | 718.8462 | 654.5879 | 625.6445 | 588.9008 | 558.5337 | 572.2779
Chart: Mesochora– Upstream
| 0.70000000000000007 | 1 | 1.5 | 2.5 | 5 | 8 | 13 | 20 | 30
WUA-Adult | 713.3829 | 917.5583 | 1184.5003 | 1487.186 | 1601.919 | 1672.0181 | 1395.491 | 1125.2547 | 1026.688
Weighted Usable area (WUA)
WUA = Σ(Ai× Ci)
Ai: is the area of a cell i
Ci : the aggregated HSI value of the cell i
Given the present curves, we could estimate that the optimum flow corresponds to 1 m3/s in Tripotamo, and 8 m3/s in Mesochora
(m 2 )
(m 2 )
Results

## Slide 17
further data collection will be necessary to extract reliable conclusions about the variation of river habitats at both low and high flows
local fish species habitat suitability curves must be developed
(and this has already begun during preliminary snorkeling surveys)
further hydrological analysis to determine the relevance of these flows in the frame of the time series of natural flow regime at each site
further analysis and validation of the models
Conclusions

## Slide 18
Hellenic Center for Marine Research
Institute of Marine Biological Resources and Inland Waters
Website: http://imbriw.hcmr.gr/en/
http://www.ecoflow.gr/en/
Thank you for your attention